## Slide 1
An Overview of Energy System Modelling for Evaluating Energy Demand, GHG Mitigation Measures & Scenarios – LEAP and Other Platforms

## Slide 2
Notes: What do we understand by ‘models’ and ‘modelling’?

## Slide 3: What we’re Going to Talk About
Session 1
Models – some fundamentals
Models need data - so something about data
Energy System Models in Brief (LEAP, WEAP, MAED TIMES, & MSFM)
Notes: Dr Gabrial Anandarajah – UCL, UK Markal Model, TIAM etc
Paul E. Dodds and Will McDowall
UCL Energy Institute, University College London

## Slide 4: Models – Definition1
A model is an external and explicit representation of part of reality as seen by the people who wish to use that model to understand, to change, to manage and control that reality

## Slide 5: Models – Definition2
Yah but really……
It’s a just tool, preferably simple, for understanding - especially that which aids decision making. We only need this to help us work through problems which we’re not evolved to solve in our heads (We solve a lot of complicated models in our heads but not all)

## Slide 6: What Are Models in more Detail?
Reality is complex and does not explain itself
A model is an abstraction from reality
  Sets of assumptions
  Focus on key aspects of problems
  Leave out irrelevant aspects of reality
Different models suit different purposes
  Like maps
  No ‘right’ model (lots of wrong ones)
  But many useful ones
    As long as it:
      clarifies policy views
      improves transparency of policy debate
  Occam’s razor
Do not have to be quantitative

## Slide 7: How do the models actually help?
  Help to organize the information in a systematic way
  Help to handle and represent a complex system
  Helps to understand the system (eg: GHG constraint)
  Help evaluate how different courses of action impact on the system and the objectives
  How to control the system to achieve objectives
  How the system responds to different uncontrollable situations

## Slide 8: Theory, Models & Policy Decisions
How can we know whether a policy will have intended effect before we implement it?
  Experience of other countries and times
    Is experience relevant to current context?
  Need to understand how an economy or an energy system or city ‘works’
    Requires theorising
Economic or Systems or Engineering theorising = constructing models
How will the system respond to shocks, interventions or adjustments?

## Slide 9
Models are dum.
They just process data into some result given rules.
An informed vision of the future must come from the users.
They don’t sense check themselves. The users need to do this.
We can only abstract the complexity we can observe, measure or deduce within a reasonable time frame.
Limitations of Models

## Slide 10: Modelling Best Practice
Well documented
Well explained to stakeholders
Replicable methodology in the public domain
Transparent assumptions
Aggregate sensitive information so you can publish into the public domain
Data – make do with what you have to make an analysis.
Exercise caution on spending time on data improvement if returns are limited

## Slide 11: The Data Issue
“There lives a man on a river in Greenland
His name is Spjellebod
He owes more fell of louse
Than he owes fat of pork
From the north is the sand drifting”
Popular Danish song from the Middle Ages

## Slide 12
Read backwards its data from the primary source for Gerard Mercator’s first map - Jacob Ziegler’s Quae Intus had copied these place names for Greenland from Claudius Clavus

## Slide 13
2009 Energy Balance
A single line item seems to be to blame. SA does not really have navigable rivers so this is likely an inadvertent entry error

## Slide 14: A Bottom-up Model of the Vehicle Parc vs Nigerian National Petroleum Commission Stats
+/- 3700 ktoe

## Slide 15
Data – A Useful Motto
“The paranoid survive.” Anonymous

## Slide 16: Not having data is not an excuse for not modelling
Mercator went on to make the most accurate maps of his day but more importantly he designed the projection we use to ‘flatten’ maps onto 2 dimensions that we use today
His mentor and collaborator on his early world maps, Gemma Frisius proposed both the method of surveying by triangulation and the method John Harrison eventually used to measure longitude.
These great models were based on a vision of what data would ultimately be available such that answers would get better and better. Coherent frameworks are more important than data.

## Slide 17: The Importance of Stakeholder Consultation
Aristotle – The habitable world is confined to the temperate zone between the northern frigid zone and the uninhabitably hot ‘torrid zone’
Vespucci – “by this voyage of mine, the opinion of the majority of philosophers is confuted…Far from being too hot for human habitation, the fresher and more temperate air of the torrid zone had attracted such a large population that more were living in it that outside of it”
“Rationally, let it be said in a whisper, experience is certainly worth more than theory”
Amerigo Vespucci, early 16th century

## Slide 18: Energy System Models – represent & cost entire energy system – some find cost optimal pathways under constraints

## Slide 19: Bottom-up Models & Useful Energy
Bottom-up allows analysis of impacts of structural change in the demand driven by socio-economic development (e.g. car ownership) and behavioural change (e.g. mode choice), fuel prices and possibilities for substitution, and technological costs and evolution – needed for long term planning where such changes don’t necessarily follow historical trends
Fuel Balanced: offers a robust way of calibrating the model which needs numerous assumptions given that so many variables are not directly observed/measured (such as mileage and average fuel consumption)

## Slide 20: Energy System (illustrative example)
Technology /Fuel Competition at Secondary & Primary Level
Notes: Represent whole energy system of commodities linked to technologies
These form alternative pathways for supplying energy services
Also enables us to see the knock-on effects of decisions in one sector on another sector in the energy system
Horizontal integration – the reference energy system links supply and demand from left to right
The energy services in different sectors integrate vertically drawing from the same primary energy sources and in some cases secondary energy sources

## Slide 21: Energy model components
Made up of 2 simple components:
  Energy Carriers (e.g. fuels, demand)
  Technologies (e.g. Light bulb, power plant) all characterized in the same way:
  Input and Output Carrier
  Efficiency
  Investment Costs per unit of capacity
  Activity Costs
  Existing Capacity
  Annual Availability
  Expected Life
  Emissions

## Slide 22: Projecting demand: Types of approaches
Trend forecasting (final)
Econometric forecasting (final)
End-use forecasting (useful)

## Slide 23: Type of energy models used for long-term planning
Energy system models
Energy models
Economic models
Focus on the energy system alone
Description of large number of single energy technologies
Capturing dynamics of the system, such as substitution of energy carriers, energy savings or technology deployment
Typical results: energy consumption, energy technology mix and capacities, emissions
Relationship of the energy sector to the general economy central element
Energy system described in a highly aggregated way
Technologies embedded in production functions
Typical results: energy consumption, emissions, GDP, employment, trade balance

## Slide 24: Universe of energy models
MAED
MSFM (Municipal)
TRACE

## Slide 25: Models – Some Comments on Platforms
MAED accessible and free. Some drawbacks – Transport demand linked to population via distance per person & not to GDP.
MESSAGE free but can’t really cope with Demand Side optimisation.
LEAP has good support from SEI and can link to the basin model WEAP for hydro impacts. Power sector optimisation and option to use CPLEX.
TIMES well supported by IEA (ETSAP) but not free in practice. More complicated to learn.
There are many teams around the world linking these platforms to macro-economic models (CGE, DSGE) and even to land-use models or technical power system models (dispatch and transmission models eg German Network Development Plan)

## Slide 26: Models – General
Having said that lack of data is not an excuse…
These aggregate systems models are only as good as the supporting micro-analysis. They are live projects that need years of development for best results. Transport for example:
Energy Systems Model
Supporting Analysis

## Slide 27
Thank You
Notes: N: e.g. Number of households
P: e.g. 70% use fridges
M: e.g. number of tons of a product produced

## Slide 28: End-use forecasting
Ei = Qi.Ii,
Qi = quantity of energy service i,
Ii = intensity of energy use for energy service i
Notes: N: e.g. Number of households
P: e.g. 70% use fridges
M: e.g. number of tons of a product produced

## Slide 29: Quantity Q
Can be decomposed in different ways depending on level of detail required and available data
Example of Qi decomposition: Qi = Ni.Pi.Mi
Ni = number of customers eligible for end-use i,
e.g. Number of households
Pi = penetration of end use i
e.g. 80% have TVs
Mi = magnitude or extent of end-use i
e.g. average hours of use of TV’s

## Slide 30: Intensity Ii
Intensity can either:
  Be in terms of final energy per unit of Qi
  e.g. kWh of electricity consumed per m2 of office space
  Be in terms of useful energy per unit of Qi
  e.g. lumens of light required per m2 of office space, in which case Qi must contain the efficiency/conversion factor from kWh to lumens

## Slide 31: In Summary
Source – IAEA Energy Expansion Handbook

## Slide 32: In practice: a combination of the methods are often used
E.g. Office illumination
E = Q.I (.P-b)
Q = Area.Mlight
Mlight = hours of lighting
Area = a.GDPb (in m2, where a,b are coefficients)
I = power density in W/m2
P = price, b = demand price elasticity

## Slide 33: Useful energy demand
Calibrated using current consumption (energy balance with adjustments, household survey, vehicle parc, bottom up estimates, other e.g. company reports)
Useful energy calculated for base year using base year assumptions (estimated technology mix)
Projected into future
    GDP assumptions
    Structure of the economy
    Changes in per capita income
    Assumed income distribution, electrification etc

## Slide 34: How to Compare the cost of Competing Energy Technologies?
When they have different
  Investment costs
  Fuels
  Efficiencies
  Maintenance costs
  Life-spans
  Load Factors / Capacity Factors / Availabilities (max Load Factor)

## Slide 35: LCOE Calculation:What Electricity Price makes Costs = Revenues?
Costs:
Revenues:
If Pricet is constant then Revenues:
Notes: Other: Decommissioning, Salvage value

## Slide 36
Costs = Revenues
LCOE =
LCOE Calculation:What Electricity Price makes Costs = Revenues?
Optimisation Models minimise the Discounted System Cost under constraint using this method
Notes: Other: Decommissioning, Salvage value

## Slide 37
Optimisation Model Builds Lowest Marginal Cost Technology
Notes: Other: Decommissioning, Salvage value

## Slide 38
Optimisation Model Builds Lowest Marginal Cost Technology
Notes: Other: Decommissioning, Salvage value

## Slide 39: Cost Parameters: O&M and Fuel
Operation and Maintenance (O&M)
  Fixed O&M: Irrespective of how many hours of operation per year.
  e.g. Staffing costs, licensing, insurance, annual shutdown.
  Variable O&M: Proportional to the number of hours of operation per year.
  e.g. maintenance equipment and material, water.
Fuel Costs/yr: Fuel Price x Units of fuel consumed/yr
Fuel Costs per unit of output =

## Slide 40: Cost Parameters: Investment t – Capital Costs
Investment a function of
Overnight construction costs
Interest during construction (IDC) , also called AFUDC (Allowance for Funds Used During Construction) is a function of construction duration, and the discount rate (cost of capital)
Overnight construction costs consists of
Owner’s costs [e.g. Site evaluations, Environmental Impact Assessment, Preliminary Engineering, Permitting and Licensing, Project Management, Site Preparation, connection to grid]
EPC costs [Final Engineering, Overall Structures, Equipment (Reactor plant, turbine plant, electric plant, pump systems), Construction labor, Construction services, Risk contingency, Start-up & Check-out, Simulation and operator training]

## Slide 41: Investment Cost breakdown for a nuclear plant
IDC: Interest during construction (or AFUDC)
Owner’s costs
EPC costs
Total Investment
Costs
Overnight costs

## Slide 42: Sectors
Sector | Disaggregation | Driver
Agriculture | By end use: irrigation, transport etc | Agriculture GDP
Residential | High, medium and low income/ electrified and non-electrified | Population, Household income, electrification
 | By end use: cooking, lighting etc | 
Commercial | By end use: lighting, HVAC, etc | Commercial GDP, building stock
Industrial | By sector: Iron and Steel, Pulp and paper etc | Sectoral Value Added or Output
 | By end use: thermal fuel or electricity (compressed air, cooling, motive, etc | 
Transport | By Sector: Air, Freight, Passenger, Pipeline | Transport GDP, Population and household income
 | By end use - Freight: rail, road (light, medium, heavy) | 
 | By end use – Passenger: Cars, SUV, bus, etc… | 

## Slide 43: LEAP – Bottom-up Demand Projection

## Slide 44: Typical LEAP Output
Based on growing economy and population
GDP
Pop.

## Slide 45: Energy Water Nexus Models - WEAP
NB: LEAP & WEAP can be linked

## Slide 46: WEAP – Hydro Variability
Calibrate model to historical output and then impose change

## Slide 47: MAED – Model for Analysis of Energy Demand (IAEA)
Notes: Freely distributed spreadsheet model
Developed by the IAEA
Quite data intensive – technology and economic data

## Slide 48: TIMES
TIMES is a partial equilibrium model that details the energy sector but does not determine the effect of decisions on the rest of the economy which may feedback
The optimiser finds a least cost solution for supply to meet demand but we can’t be totally sure that the solution is the least cost to the whole economy without linking to or integrating with an economic model.
The same would be true of an agricultural or land use model that is in partial equilibrium

## Slide 49: Main Features
Bottom-up Energy Systems Optimization Long-Range (>10 years) Planning Model (similar to the one used for the IEP)
Full Sector: Includes and allows trade-off between demand and Supply
End-use type model:
  Gives a detailed description of how the energy is used.
  Describes the types of equipment used and how much energy is used by each type of equipment to satisfy demand.
  Can be used to forecast useful energy as well as final energy demand
  Can capture:
    structural changes/ shocks
    mode switching (transport)
    fuel switching
    Technical improvement/ improved efficiency
    Intensity changes e.g. mines have to dig deeper

## Slide 50: TIMES Output – Cost Optimal New Build Plan

## Slide 51: TIMES Output – The Relative Price Given New Build Plan

## Slide 52: Municipal Services Financial Model (MSFM)
Investment requirements over 10 years
How investments may be financed
Impacts on operating account
Infrastructure Investment tool
What is the need for capital expenditure?
What can we afford to spend?
How is this going to impact on our on-going financial viability?
Notes: Developed by Consultants – PDG
Spreadsheet based – has many counterparts in many organisations

## Slide 53
MUNICIPALITY
Settlement types
Low income households
High income households
Non-residential
consumers
TECHNICAL DATA
BUDGET
PROVIDERS
SERVICE LEVELS
CONSUMPTION
UNIT COSTS
INDIGENCE POL.
SUBSIDIES
ASSETS
FINANCE STRAT.
OP COST
CAP COST
RESOURCES
DEMOGRAPHIC GROWTH
ECONOMIC GROWTH
SERVICE DELIVERY
SUBSIDIES
TARIFFS
COSTS
DEMAND MAN.
FINANCING STRATEGY

## Slide 54: Projected capital expenditure
R21 billion in over 10 yrs - 55% for rehabilitation

## Slide 55: Projected operating expenditure
Driven almost entirely by bulk tariff

## Slide 56: Projected net operating position
Surpluses of 16% to 11% of revenue over the 10 years
Assumes surcharge on bulk tariff remains constant

## Slide 57: Tool for Rapid Assessment of City Energy (TRACE)
Notes: Browser application
Less intensive
World Bank
Focussed on Energy Efficiency Measures

## Slide 58: TRACE – Comparative Database of Cities

## Slide 59: TRACE – Prioritize Efficiency Measures