## Slide 1: A Tool for Energy Planning and GHG Mitigation Assessment

## Slide 2: Using Models for LEDS: Important Considerations
Modeling sophistication is less important than the rigor, consistency and data quality underpinning the analysis itself. “GiGo”
Consider who will undertake the analysis. Outside consultants provide ready source of expertise, but may do little to build capabilities in-house.
Even relatively simple models require many months and a good level of expertise.
Modeling and policy policy analysis requires strong guidance from local experts and buy-in from high level decision makers. Too important to be left to only modelers!
Strong, coordinated and diverse team needed: economists, engineers, energy & industrial engineers, agriculture etc.
Ideally setup up a permanent team responsible for LEDS modeling to ensure continuity of expertise.
Close coordination needed with other national groups: e.g. those working on GHG inventories and those doing national energy planning.

## Slide 3: Types of Models
Both Top-Down and Bottom-up models can yield useful complementary insights on mitigation.
They are the two basic approaches to examine the linkages between the economy and specific GHG emitting sectors such as the energy system.
Top-down models evaluate the system from aggregate economic variables:
  Most useful for studying broad macroeconomic and fiscal policies for mitigation such as carbon or other environmental taxes.
whereas Bottom-up models consider technological options or project-specific climate change mitigation policies:
    Most useful for studying options that have specific sectoral and technological implications.

## Slide 4: Types of Top-Down Models
CGE (Computational General Equilibrium) models use economic data to estimate how an economy will respond to changes in policies, technologies and prices.
Input/Output models focus on interdependencies among different sectors of an economy.
Integrated Assessment Models: Tend to be based on physical/technological descriptions of systems and their interconnections (energy, water, land, agriculture, forestry, food, etc.).
Top-down
CGE
Input-Output
Other Macro Models
Integrated Assessment Models
Notes: Talking points:
Integrated Assessment Models are really more physical than economic because are based in physical accounting. But they also tend to be at the macro scale and less suited for national-level mitigation assessment, so they have been included here.
Background information
CGE Models
  Simplified definitions: http://en.wikipedia.org/wiki/Computable_general_equilibrium
  Technical definitions: http://rri.wvu.edu/CGECourse/Sue%20Wing.pdf
  CGE models are sometimes also called AGE (applied general equilibrium) models
I/O Models
  Simplified definitions: http://en.wikipedia.org/wiki/Input-output_model
  Specific example: http://www.iioa.org/pdf/Intermediate-2008/Papers/1c1_Matthews.pdf
OECD Modeling:
  General information: http://www.uncsd2012.org/rio20/content/documents/presentation%20ENV-Linkages%20RobD.pdf
  Specific paper: http://ideas.repec.org/p/sur/seedps/115.html
Cambridge Economics - http://www.camecon.com/ModellingTraining/suite_economic_models/E3MG.aspx
IMAGE/TIMER Model: http://www.pbl.nl/en/publications/2001/TheTargetsIMageEnergyRegionalTIMERModelTechnicalDocumentation
PoleStar: http://www.polestarproject.org/polestar_sys.html

## Slide 5: Types of Bottom-Up Energy Sector Models
Optimization: Use mathematical programming to identify configurations of energy systems that minimize the total cost of providing services. EG: MARKAL/TIMES, LEAP, MESSAGE
Simulation: Simulate behavior of consumers and producers under various signals (e.g. price, income levels) and constraints (e.g. limits on rate of stock replacement). EG: ENPEP-BALANCE
Accounting Frameworks: Account for physical stocks and flows in systems based primarily on engineering relationships and explicit assumptions about the future (e.g. technology improvements, market penetration rates). EG: LEAP, EFFECT, MAED
Technology Screening: Focus on how a particular technology (or set of technologies) will perform under certain constraints and can track associated costs and emissions. EG: RETScreen, HOMER. ClimateDesk
Bottom-up
Optimization
Simulation
Accounting
Technology Screening

## Slide 6
Long-range Energy Alternatives Planning System: 1982-Present
Easy-to-use, graphical, scenario-based modeling software for energy planning and GHG mitigation assessment.
Broad scope, low initial data requirements, flexible data structures.
A comprehensive decision support tool for creating models of different energy systems.
Becoming de facto standard for developing countries’ energy planning, national communications, low emission development strategies (LEDS), and national action planning on SLCPs.
Useful at different scales: cities, states, countries, regions, globally.
Long-range perspective, annual time step with seasonal/time-of-day details.

## Slide 7
Integrated watershed hydrology and water planning model
GIS-based, graphical drag & drop interface
Physical simulation of water demands and supplies
Works in concert with LEAP for nexus applications.

## Slide 8: www.energycommunity.org
Free online community supporting developing country sustainability planners.
Started in 2000. Now has >20,000 members in 191 countries.
Discussions & support forums.
Social network connects LEAP users around the world based on their interests and location.
Library containing useful resources for planners and modelers; lists of academic courses.
Download LEAP and get guidance on other related models.
Access LEAP training and reference materials.
Free national-scale LEAP data sets for 105 countries.
News about LEAP and trainings.
English, Spanish, French Chinese.
Automatically administers LEAP licenses and downloads.
Enables SEI to see who is using LEAP in real time (important for funders).
Main tool for providing LEAP technical support and help desk.
Coming soon: Support for SLCP National Action Planning.

## Slide 9: How Does LEAP Compare to Other Energy Models?
Other tools typically have more sophisticated energy modeling capabilities, but are harder to use, more data intensive.
LEAP’s focus is on transparency of results, ease-of-use, data flexibility, adaptability to different scales, data & scenario management and reporting.
Notable for the degree of methodological choices it provides to users.
Ability to link to other models and software through its API.

## Slide 10: Copenhagen Climate Plan, 2009
The Consulting Company RAMBOLL used LEAP to prepare a plan for the city of Copenhagen to become CO2 neutral by 2025.
Copenhagen is already perhaps the most energy efficient city in the World, in part due to its widespread use of CHP systems for district heating and huge investments in wind power, and because nearly 40% of its citizens cycle to work or school every day.
This study formed the basis for Copenhagen setting a target of 20% reduction in CO2 emissions by 2015 compared to 2005 and becoming completely CO2 neutral by 2025.

## Slide 11: APEC: Energy Demand and Supply Outlook 2009, 2006, 2002
Forecasts demand and supply for each APEC economy. Updated every 3-4 years
Examines key technical and socio-economic drivers in APEC such as urbanization, aging of populations, relocation of industries towards less developed economies, technology development.
Draws policy implications regarding the future energy demand and supply in the APEC region.
Data and Methods:
Key time-series from IEA supplemented by national & APEC statistics, and World Bank indicators.
Top-down econometric approach used to project energy demands. Microfit used to develop econometric equations, which are then entered in LEAP.
LEAP used to model Transformation, to create scenario projections and to generate supply and demand balance tables.

## Slide 12: The Massachusetts Clean Energy and Climate Plan (CECP), 2010
The Global Warming Solutions Act (GWSA) requires MA to achieve GHG reductions of 80% by 2050 vs. 1990.
The Commonwealth of Mass asked SEI to use LEAP to model a portfolio of options capable of meeting that goal.
For 2050, 40+ policies examined including system and end-use efficiency, electrification, low carbon fuels and lifestyles.
Results used to inform the State Government’s Clean Energy and Climate Protection plan: published in 2010.
tinyurl.com/CECPMass

## Slide 13: More examples at:
www.energycommunity.org/apps

## Slide 14
LEAP: User Interface

## Slide 15: LEAP Structure & Calculation Flows

## Slide 16: Main Components of a LEAP Analysis
Energy Demand Analysis
Energy Conversion and Resources (Transformation)
Emissions (GHGs and Local Air Pollutants)
Cost-Benefit Analysis
Non-energy Sector Emissions

## Slide 17: Tutorial
Exercise 1 will introduce you to the basic elements of energy demand and supply analysis, of projecting energy requirements and calculating environmental loadings
Exercises 2 and 3 allow you to develop a basic energy analysis, to create scenarios, and to evaluate a handful of individual policy and technical options, such as cogeneration, energy efficiency standards, and switching power plants from coal to natural gas.
Exercise 4 lets you explore the costs and benefits of several alternative scenarios. Scenarios are implemented on both the demand and supply side, and you will explore LEAP’s Cost-Benefit calculator to find the costs of reducing emissions under each scenario. Exercise 4 requires that you begin with a completed version of Exercise 3.

## Slide 18: Demand Analysis in LEAP
Analysis of energy consumption and associated costs and emissions in an area.
Demands organized into a flexible hierarchical tree structure.
Typically organized by sector, subsector, end-use and device.

## Slide 19: The Tree
The main data structure used for organizing data and models, and reviewing results
Icons indicate types of data (e.g., categories, technologies, fuels and effects)
User can edit data structure.
Supports standard editing functions (copying, pasting, drag & drop of groups of branches)

## Slide 20: A Simple Demand Data Structure
Households
(8 million)
Cooking
(100%)
Refrigeration
(80%)
Lighting
(100%)
Existing (80%, 400 kWh/yr)
Urban (30%)
Rural (70%)
Efficient (20%, 300kWh/yr)
Other
(50%)
Electrified (100%)
Electrified (20%)
Non-Electrified (80%)
The tree is the main data structure used for organizing data and models, and for reviewing results.
Icons indicate the types of data (e.g., categories, technologies, fuels and environmental effects).
Users can edit the tree on-screen using standard editing functions (copy, paste, drag & drop)
Structure can be detailed and end-use oriented, or highly aggregate
Detail can be varied from sector to sector.

## Slide 21: Transformation Analysis in LEAP
Analysis of energy conversion, transmission and distribution, and resource extraction.
Basic hierarchy: “modules” (sectors), each containing one or more “processes”, which represent an individual technology such as a particular type of electric plant or oil refinery, and produces one or more output fuels. These represent the energy products produced by the module such as electricity or heat.
Each process can have one or more feedstock fuels and one or more auxiliary fuels.
Calculates imports, exports and primary resource requirements.
Tracks costs and environmental loadings.

## Slide 22: General Transformation Module Layout

## Slide 23: A Transformation Module for Electricity Generation

## Slide 24: A Transformation Module for Oil Refining

## Slide 25: Electric Generation
Two Issues to consider:
Capacity Expansion: How much capacity to build and when? (MW)
Dispatch: Once built, how should the plants be operated? (MW-Hr)

## Slide 26: Load-Duration Curve and System Dispatch in LEAP
Intermediate Load Plants
Baseload Plants
Peak Load Plants
Capacity (MW) * MCF
Hours Sorted from Highest to Lowest Demand
8,500
8,000
7,500
7,000
6,500
6,000
5,500
5,000
4,500
4,000
3,500
3,000
2,500
2,000
1,500
1,000
500
0
Percent of Peak Load
100
95
90
85
80
75
70
65
60
55
50
45
40
35
30
25
20
15
10
5
0
A LDC is similar to a load curve but the demand data is ordered in descending order of magnitude, rather than chronologically.
It shows the capacity utilization requirements for each increment of load.
The area under the curve represents the energy demanded by the system.

## Slide 27: Electric Generation Dispatch
Plants are dispatched to meet both total demand (in MWh) as well as the instantaneous peak demand which varies by hour, day and season.
User can exogenously specify a load-duration curve and LEAP will dispatch plants by merit order.
Alternatively, load shapes be specified for each demand device so that the overall system load is calculated endogenously. Thus the effect of DSM policies on the overall load shape can then be explored in scenarios.
Plant dispatch can also then be varied by season (e.g. to reflect how hydro dispatch may vary between wet and dry seasons).

## Slide 28: Emissions Accounting
Emission factors for any GHG or local air pollutant can be entered in LEAP and used to calculate emissions loadings.
Can be specified in any physical unit and can be denominated by units of either energy consumption or production (e.g. kg/ton of coal) or distance driven for transport factors (e.g. grams/mile).
Can also be specified in terms of the chemical composition of fuels (e.g. sulfur): automatically adjusts standard emission factors based on specific fuels used in the study area.
Includes default IPCC “Tier 1” emission factors for GHG inventories.
Results can be shown for individual pollutants or summed to show overall Global Warming Potential (GWP).

## Slide 29: Energy Balances in LEAP
Results automatically formatted as standard energy balance tables.
Balances can be viewed for any year, scenario or region in different units.
Balance columns can be switched among fuels, fuel groupings, years, and regions.
Balance rows are the Demand and Transformation sectors. Optionally can show subsectoral results
Displays results in any energy unit.
Results in table, chart, or energy flow diagram formats.

## Slide 30: Energy Balances
Net Changes in Stocks
Non-energy consumption (e.g. petrochemical feedstock, fertilizers)
Imports
Exports
Transformation Sectors Losses and Consumption
Total Primary Energy Produced
Total Final Energy Use in Consuming Sectors
An accounting system that describes the flows of energy through an economy, during a given period.
Notes: The name “balance” refers to the fact that the quantities of primary energy produced must be equal to the quantities consumed, after accounting for changes in stocks, imports and exports and the share used for conversion into secondary energy carriers, including losses.

## Slide 31: Social Cost-Benefit Analysis in LEAP
Societal perspective of costs and benefits (i.e. economic not financial analysis).
Avoids double-counting by drawing consistent boundary around analysis (e.g. whole system including.
Cost-benefit analysis calculates the Net Present Value (NPV) of the differences in costs between two scenarios.
NPV sums all costs in all years of the study discounted to a common base year.
Optionally includes externality costs, decommissioning costs and costs of unserved demands.

## Slide 32: LEAP Data Requirements
Low initial data requirements..
LEAP itself is very flexible in terms of what data it can accept.
Different levels of detail can be used in each different sector.
However, serious analyses do of course require good and reasonably plentiful and up-to-date information.

## Slide 33: Types of Data that can be Used in LEAP

## Slide 34: Expressions
Fundamental to how data is entered and managed across scenarios and regions in LEAP.
Similar to expressions in spreadsheets.
Used to specify the value of variables.
Expressions can be simple numerical values, or a formula that yields different results in each year.
Can make use of many built-in functions, or refer to the values of other variables.
Can be linked to Excel spreadsheets.

## Slide 35: Expression Examples
Simple Number
  Calculates a constant value in all scenario years.
Simple Formula
  Example: 0.1 * 5970
Growth
  Example: Growth(3.2%)
  Calculates exponential growth over time.
Interpolation
  Example: Interp(2000, 40, 2010, 65, 2020, 80)
  Calculates gradual change between data values
Step
  Example: Step(2000, 300, 2005, 500, 2020, 700)
  Calculates discrete changes in particular years
GrowthAs
  Example: GrowthAs(Income,elasticity)
  Calculates future years using the base year value of the current branch and the rate of growth in another branch.

## Slide 36: Key Assumptions
Key Assumption Variables are used for creating additional user-defined variables such as macroeconomic, demographic and other time-series variables.
Can hold exogenous variables (input assumptions) and can also be used to calculate intermediate results using LEAP’s expressions.
You can also add your own User Variables which are visible in the Demand, Transformation and Resource branches, and Indicator Variables: which are used to calculate additional results after all other LEAP calculations are complete.