## Slide 1: LEAP software and energy modelling workshop

## Slide 2: Overview of this CPD LEAP workshop
This session:
  LEAP in SAMSET
  Briefly – about modelling
  LEAP exercise 1 – begin making your own energy model
Friday session (CPD day 5)
  Investigate your own scenario in a LEAP model of Jinja

## Slide 3: LEAP in SAMSET
5 new LEAP city/municipal models – 2 in Ghana, 2 in Uganda, and 1 in South Africa (plus 1 update to Cape Town)
SAMSET partners – surveys to collect data
ERC develop data into LEAP to create energy system model of these cities
State of Energy reports, LEAP modelling technical reports

## Slide 4: Model definition 1
A model is an external and explicit representation of part of reality as seen by the people who wish to use that model to understand, to change, to manage and control that reality

## Slide 5: Model definition 2…
Yah but really……
It’s a just tool, preferably simple, for understanding - especially that which aids decision making. We only need this to help us work through problems which we’re not evolved to solve in our heads (We solve a lot of complicated models in our heads but not all)

## Slide 6: Theory, Models & Policy Decisions
How can we know whether a policy will have intended effect before we implement it?
  Experience of other countries and times
    Is experience relevant to current context?
  Need to understand how an economy or an energy system or city ‘works’
    Requires theorising
Economic or Systems or Engineering theorising = constructing models
How will the system respond to shocks, interventions or adjustments?

## Slide 7: Using Models for LEDS/Sustainability/Planning: Important Considerations
Modeling sophistication is less important than the rigor, consistency and data quality underpinning the analysis itself. “GiGo”
Consider who will undertake the analysis. Outside consultants provide ready source of expertise, but may do little to build capabilities in-house.
Even relatively simple models require many months and a good level of expertise.
Modeling and policy policy analysis requires strong guidance from local experts and buy-in from high level decision makers. Too important to be left to only modelers!
Strong, coordinated and diverse team needed: economists, engineers, energy & industrial engineers, agriculture etc.
Ideally setup up a permanent team responsible for LEDS modeling to ensure continuity of expertise.
Close coordination needed with other national groups: e.g. those working on GHG inventories and those doing national energy planning.

## Slide 8: Limitations of models
Models are dumb.
They just process data into some result given rules.
An informed vision of the future must come from the users.
They don’t sense check themselves. The users need to do this.
We can only abstract the complexity we can observe, measure or deduce within a reasonable time frame.

## Slide 9: Types of Models
Both Top-Down and Bottom-up models can yield useful complementary insights on mitigation.
They are the two basic approaches to examine the linkages between the economy and specific GHG emitting sectors such as the energy system.
Top-down models evaluate the system from aggregate economic variables:
  Most useful for studying broad macroeconomic and fiscal policies for mitigation such as carbon or other environmental taxes.
whereas Bottom-up models consider technological options or project-specific climate change mitigation policies:
    Most useful for studying options that have specific sectoral and technological implications.

## Slide 10: Types of Top-Down Models
CGE (Computational General Equilibrium) models use economic data to estimate how an economy will respond to changes in policies, technologies and prices.
Input/Output models focus on interdependencies among different sectors of an economy.
Integrated Assessment Models: Tend to be based on physical/technological descriptions of systems and their interconnections (energy, water, land, agriculture, forestry, food, etc.).
Top-down
CGE
Input-Output
Other Macro Models
Integrated Assessment Models
Notes: Talking points:
Integrated Assessment Models are really more physical than economic because are based in physical accounting. But they also tend to be at the macro scale and less suited for national-level mitigation assessment, so they have been included here.
Background information
CGE Models
  Simplified definitions: http://en.wikipedia.org/wiki/Computable_general_equilibrium
  Technical definitions: http://rri.wvu.edu/CGECourse/Sue%20Wing.pdf
  CGE models are sometimes also called AGE (applied general equilibrium) models
I/O Models
  Simplified definitions: http://en.wikipedia.org/wiki/Input-output_model
  Specific example: http://www.iioa.org/pdf/Intermediate-2008/Papers/1c1_Matthews.pdf
OECD Modeling:
  General information: http://www.uncsd2012.org/rio20/content/documents/presentation%20ENV-Linkages%20RobD.pdf
  Specific paper: http://ideas.repec.org/p/sur/seedps/115.html
Cambridge Economics - http://www.camecon.com/ModellingTraining/suite_economic_models/E3MG.aspx
IMAGE/TIMER Model: http://www.pbl.nl/en/publications/2001/TheTargetsIMageEnergyRegionalTIMERModelTechnicalDocumentation
PoleStar: http://www.polestarproject.org/polestar_sys.html

## Slide 11: Types of Bottom-Up Energy Sector Models
Optimization: Use mathematical programming to identify configurations of energy systems that minimize the total cost of providing services. EG: MARKAL/TIMES, LEAP, MESSAGE
Simulation: Simulate behavior of consumers and producers under various signals (e.g. price, income levels) and constraints (e.g. limits on rate of stock replacement). EG: ENPEP-BALANCE
Accounting Frameworks: Account for physical stocks and flows in systems based primarily on engineering relationships and explicit assumptions about the future (e.g. technology improvements, market penetration rates). EG: LEAP, EFFECT, MAED
Technology Screening: Focus on how a particular technology (or set of technologies) will perform under certain constraints and can track associated costs and emissions. EG: RETScreen, HOMER. ClimateDesk
Bottom-up
Optimization
Simulation
Accounting
Technology Screening

## Slide 12
Long-range Energy Alternatives Planning System: 1982-Present
Easy-to-use, graphical, scenario-based modeling software for energy planning and GHG mitigation assessment.
Broad scope, low initial data requirements, flexible data structures.
A comprehensive decision support tool for creating models of different energy systems.
Becoming de facto standard for developing countries’ energy planning, national communications, low emission development strategies (LEDS), and national action planning on SLCPs.
Useful at different scales: cities, states, countries, regions, globally.
Long-range perspective, annual time step with seasonal/time-of-day details.

## Slide 13: Hands on…

## Slide 14: (Second LEAP session) Modelling scenarios
Planners have a question or curiosity about the impact of a new or different policy/behaviour/intervention in the current Business as Usual
  “How much charcoal would be saved from a charcoal efficient stove program? How much money would this save? What impact does it have on
  air pollution (and health)?”
  Would BRTs be more energy efficient than current public transport?
  “How much fuel (and/or money) would be saved from people carpooling to work?”

## Slide 15: Background on the model you will be using
Background... SAMSET Jinja model. Data survey come from.. A major corridor route.
Numbers…

## Slide 16: Explore the LEAP model
To get an idea of what detail there is, have a look at the [LEAP model]

## Slide 17: Making your own scenario
Come up with a scenario idea you are curious about:
Briefly write out the scenario you want to investigate
  Once written, stop and ask for some feedback about your idea
Write down the assumptions and associated parameters this scenario involves (cost, fuel savings/efficiency improvements)
  Ask for help if you need with this
  Once finished, stop and ask for feedback and input on this

## Slide 18: How to make a scenario in LEAP
Click on ‘Scenarios’ tab on the top pane next to ‘General Parameters’
Click on the + sign and type in a short name of your scenario
  Now LEAP has made a copy (internally) of your model, and you can now proceed to change numbers associated with your scenario.
To change numbers in your model for this scenario, go to Scenario drop down list and select your scenario: