## Slide 1: South Africa’s proposed nuclear build plan: an analysis of the potential socioeconomic risks
Tara Caetano
Energy Research Centre
9 March 2016
The Economics of Nuclear Energy Workshop

## Slide 2: Motivation
IRP 2010 effectively forced a full fleet of 9,6GW of nuclear into the final electricity build plan
The IRP Update on nuclear:
  “...demand may not reach the levels required which raises the risk of overbuilding generation capacity”
  “…uncertainties suggest …a more flexible approach taking into account different outcomes based on changing…...scenarios and……in making key investment decisions”
  “The nuclear decision can possibly be delayed…..and there are alternative options such as regional hydro…..before prematurely committing to a technology that may be redundant…..”
Notes: The study reviews this commitment in comparison to a more flexible planning approach to energy planning that is guided by the imperative of minimising costs. Concisely stated our analysis seeks to answer the following research questions:
Evaluating THE nuclear programme, not A nuclear programme.
Could list all the uncertainties – drawn from another study.

## Slide 3: Research questions
RQ1: Given the high level of uncertainty inherent in long-term electricity planning, how does the commitment to 9.6GW of nuclear power by 2030 compare to a more flexible planning approach in meeting government’s stated objectives of economic growth, job creation, and welfare?
RQ2: If we do commit to 9.6 GW of nuclear power what are the risks of an electricity price increase and associated socioeconomic implications?

## Slide 4: Three tiers of research
RQ2
Future 1
Commitment to nuclear power
Flexible planning approach
Future 2
Commitment to nuclear power
Flexible planning approach
RQ1
Monte Carlo Analysis
Future....
Future...
Future...
Commitment to nuclear power
Flexible planning approach
Commitment to nuclear power
Flexible planning approach
Commitment to nuclear power
Flexible planning approach

## Slide 5: Increase in electricity price for 1000 plausible futures…
94% chance that the electricity price will be greater with the commitment to nuclear power in 2030
20% chance that the price will be at least 10% higher
Future 1
Future 2

## Slide 6: Main uncertainties and assumptions

## Slide 7: Zooming in on Future 1
Nuclear at $5100/kW does come in before 2030, but only 4GW
17.8GW by 2040
Over 20GW of CSP installed capacity in both scenarios

## Slide 8: Zooming in on Future 1

## Slide 9: Zooming in on Future 2
Delays: First unit in 2031
No new nuclear with flexible planning
CSP preferred at a cost of $7000/kW for nuclear
Imported hydro and shale gas

## Slide 10: Zooming in on Future 2
Sustained high electricity prices and crowding out of investment

Non-ferrous metals (-0.44% per annum)
Iron and steel (-0.21% per annum)
Metals (-0.17% per annum)
75 000 jobs at risk
Consumers are hit directly by electricity prices and by overall decreased growth

## Slide 11: Conclusions
Our results show that there is no economic case to be made for procuring the full 9.6GW of nuclear power by 2030.
High risk of electricity price increases with the commitment to nuclear power – 95th percentile.
As mentioned in the IRP Update and confirmed by our results, a flexible planning approach should be adopted.
The electricity build plan must reflect and balance the expected electricity demand, consider least-cost alternatives and ensure the provision of affordable electricity.
“Only procure nuclear at a scale and pace at which the country can afford.”

## Slide 12: Electricity demand
Chart: Annual Expected Electricity Consumption - upstream of transmission (TWh)
| 2015.0 | 2016.0 | 2017.0 | 2018.0 | 2019.0 | 2020.0 | 2021.0 | 2022.0 | 2023.0 | 2024.0 | 2025.0 | 2026.0 | 2027.0 | 2028.0 | 2029.0 | 2030.0 | 2031.0 | 2032.0 | 2033.0 | 2034.0 | 2035.0 | 2036.0 | 2037.0 | 2038.0 | 2039.0 | 2040.0
SO IRP moderate | 285.526 | 298.332 | 310.41 | 319.523 | 327.438 | 336.178 | 340.946 | 349.164 | 358.299 | 368.136 | 377.496 | 379.871 | 391 | 402.296 | 407.175 | 416.41 | 427.572 | 440.175 | 450.03 | 460.968 | 473.203 | 486.094 | 496.368 | 507.587 | 519.276 | 530.777
Best-Least.Cost | 269.1107 | #N/A | #N/A | #N/A | #N/A | 302.4928 | #N/A | #N/A | #N/A | #N/A | 341.3122 | #N/A | #N/A | #N/A | #N/A | 383.1398 | #N/A | #N/A | #N/A | #N/A | 444.3226 | #N/A | #N/A | #N/A | #N/A | 520.2344
Green Shoots | 271.424 | 279.384 | 287.479 | 296.379 | 305.418 | 314.79 | 324.303 | 333.929 | 343.561 | 353.651 | 364.056 | 366.034 | 376.611 | 387.506 | 398.408 | 409.14 | 418.001 | 425.856 | 433.743 | 440.862 | 447.926 | 454.617 | 461.389 | 468.272 | 473.96 | 479.589
SO IRP Low | 280.652 | 290.655 | 299.726 | 305.76 | 310.512 | 315.93 | 317.499 | 322.214 | 327.658 | 333.612 | 338.997 | 337.064 | 343.747 | 350.421 | 351.357 | 356.001 | 362.172 | 369.418 | 374.193 | 379.747 | 386.231 | 393.097 | 397.687 | 402.913 | 408.379 | 413.561
Worst-Least.Cost | 269.5436 | #N/A | #N/A | #N/A | #N/A | 297.3702 | #N/A | #N/A | #N/A | #N/A | 323.1436 | #N/A | #N/A | #N/A | #N/A | 341.3837 | #N/A | #N/A | #N/A | #N/A | 372.1124 | #N/A | #N/A | #N/A | #N/A | 404.4177
Weathering the Storm | 267.139 | 272.914 | 278.506 | 284.615 | 290.616 | 296.483 | 302.448 | 308.428 | 314.556 | 320.808 | 326.798 | 323.93 | 329.588 | 334.88 | 340.317 | 344.747 | 349.065 | 353.445 | 357.608 | 361.794 | 365.469 | 369.17 | 372.897 | 376.648 | 380.425 | 384.245

## Slide 13: Cost
Chart: Total Plant Cost in 2015 US$/kW
| IRP 2010 | EPRI IRP 2010 Low | EPRI IRP 2010 High | IEA2010 US High | EPRI 2008 | EIA 2008 | EIA 2009 | Lazard Low | Lazard High | MIT 2009 | IEA2010 Eur Low | IEA 2010 Eur High | EC2008 Low | EC2008 High | IEA2010 Asia Low | IES2010 Asia High | Finland Olkiluoto | France Flamanville | China Taishan | Hinkley Point | VVER-1200 lower | VVER-1200 upper
IRP Update | 5862.78 | 4234.23 | 4885.65 | 3691.38 | 4451.37 | 3691.38 | 5645.64 | 4125.66 | 5754.21 | 4451.37 | 4234.23 | 5862.78 | 2822.82 | 4885.65 | 1628.55 | 2497.11 | 6188.49 | 5862.78 | 2714.25 | 8685.6 | 0 | 0
Actual | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 7599.9 | 7599.9 | 0 | 0 | 0 | 0
Estimated | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2714.25 | 2931.39 | 0 | 0 | 5100.1843 | 7000.2136

## Slide 14: Lead Times
Chart: 
| ANGRA-2 | DAYA BAY-1 | DAYA BAY-2 | FANGJIASHAN-1 | FUQING-1 | HONGYANHE-1 | HONGYANHE-2 | LING AO-1 | LING AO-2 | LING AO-3 | LING AO-4 | NINGDE-1 | NINGDE-2 | TIANWAN-1 | TIANWAN-2 | YANGJIANG-1 | TEMELIN-1 | TEMELIN-2 | CATTENOM-3 | CATTENOM-4 | CHOOZ B-1 | CHOOZ B-2 | CIVAUX-1 | CIVAUX-2 | GOLFECH-1 | GOLFECH-2 | PENLY-1 | PENLY-2 | KUDANKULAM-1 | TOMARI-3 | HANBIT-3 | HANBIT-4 | HANUL-3 | HANUL-4 | SHIN-KORI-1 | SHIN-KORI-2 | SHIN-WOLSONG-1 | BALAKOVO-4 | KALININ-3 | KALININ-4 | ROSTOV-1 | ROSTOV-2 | ROSTOV-3 | SIZEWELL B | KHMELNITSKI-2 | ROVNO-4 | COMANCHE PEAK-1 | COMANCHE PEAK-2 | SEABROOK-1 | WATTS BAR-1
Construction Years | 24.5151 | 6.0055 | 5.8411 | 5.9205 | 5.7507 | 5.5096 | 5.674 | 4.7589 | 4.8356 | 4.5836 | 4.9178 | 4.8356 | 5.1699 | 6.5863 | 6.6658 | 5.0027 | 13.8411 | 15.8411 | 8.0877 | 7.6685 | 12.5918 | 11.3397 | 9.1726 | 8.674 | 7.5863 | 8.6712 | 7.6685 | 7.5068 | 11.5945 | 4.3315 | 4.8356 | 5.1699 | 4.5068 | 5.0849 | 4.1699 | 4.589 | 4.1699 | 9.0055 | 19.1808 | 25.2685 | 19.5096 | 26.8521 | 5.2521 | 6.5918 | 19.5096 | 18.1808 | 15.3425 | 18.3452 | 13.8411 | 22.6027
Notes: PRIS database

## Slide 15: Capacity schedule

## Slide 16: Availability
Chart: Availability (%)
| ANGRA-2 | DAYA BAY-1 | DAYA BAY-2 | FANGJIASHAN-1 | FUQING-1 | HONGYANHE-1 | HONGYANHE-2 | LING AO-1 | LING AO-2 | LING AO-3 | LING AO-4 | NINGDE-1 | NINGDE-2 | TIANWAN-1 | TIANWAN-2 | YANGJIANG-1 | TEMELIN-1 | TEMELIN-2 | CATTENOM-3 | CATTENOM-4 | CHOOZ B-1 | CHOOZ B-2 | CIVAUX-1 | CIVAUX-2 | GOLFECH-1 | GOLFECH-2 | PENLY-1 | PENLY-2 | KUDANKULAM-1 | TOMARI-3 | HANBIT-3 | HANBIT-4 | HANUL-3 | HANUL-4 | SHIN-KORI-1 | SHIN-KORI-2 | SHIN-WOLSONG-1 | BALAKOVO-4 | KALININ-3 | KALININ-4 | ROSTOV-1 | ROSTOV-2 | ROSTOV-3 | SIZEWELL B | KHMELNITSKI-2 | ROVNO-4 | COMANCHE PEAK-1 | COMANCHE PEAK-2 | SEABROOK-1 | WATTS BAR-1
2004 - 2014 | 86.1 | 85.1 | 84.2 | 79.6 | 81.1 | 88.5 | 89.6 | 83.9 | 87.7 | 75.3 | 83.8 | 86.3 | 72.5 | 77.8 | 79.2 | 82.1 | 79.7 | 80 | 76.5 | 80.5 | 82.5 | 83.6 | 81 | 82.3 | 43.4 | 87 | 89.1 | 87.5 | 80.1 | 75.3 | 73.7 | 72.9 | 78.5 | 83.3 | 81.5 | 87.2 | 90.5 | 83.9 | 77.1 | 73 | 89.7 | 91.8 | 87.6 | 90.2

## Slide 17: Centralised PV

## Slide 18: CSP

## Slide 19: Wind

## Slide 21: Employment Assumptions