## Slide 1: The potential socioeconomic risks of nuclear power investment in SA
Tara Caetano & Brenda Martin
Energy Research Centre
10 May 2016
Cape Chamber of Commerce and Industry

## Slide 2: Findings from a recent ERC report: South Africa’s proposed nuclear build plan: an analysis of the potential socioeconomic risks
Tara Caetano

## Slide 3: Motivation
IRP 2010 effectively forced a full fleet of 9,6GW of nuclear into the final electricity build plan
The IRP Update on nuclear:
  “...demand may not reach the levels required which raises the risk of overbuilding generation capacity”
  “…uncertainties suggest …a more flexible approach taking into account different outcomes based on changing…...scenarios and……in making key investment decisions”
  “The nuclear decision can possibly be delayed…..and there are alternative options such as regional hydro…..before prematurely committing to a technology that may be redundant…..”
Notes: The study reviews this commitment in comparison to a more flexible planning approach to energy planning that is guided by the imperative of minimising costs. Concisely stated our analysis seeks to answer the following research questions:
Evaluating THE nuclear programme, not A nuclear programme.
Could list all the uncertainties – drawn from another study.

## Slide 4: Research questions
RQ1: Given the high level of uncertainty inherent in long-term electricity planning, how does the commitment to 9.6GW of nuclear power by 2030 compare to a more flexible planning approach in meeting government’s stated objectives of economic growth, job creation, and welfare?
RQ2: If we do commit to 9.6 GW of nuclear power what are the risks of an electricity price increase and associated socioeconomic implications?

## Slide 5: Three tiers of research
RQ2
Future 1
Commitment to nuclear power
Flexible planning approach
Future 2
Commitment to nuclear power
Flexible planning approach
RQ1
Monte Carlo Analysis
Future....
Future...
Future...
Commitment to nuclear power
Flexible planning approach
Commitment to nuclear power
Flexible planning approach
Commitment to nuclear power
Flexible planning approach

## Slide 6: Increase in electricity price for 1000 plausible futures…
94% chance that the electricity price will be greater with the commitment to nuclear power in 2030
20% chance that the price will be at least 10% higher
Future 1
Future 2

## Slide 7: Main uncertainties and assumptions

## Slide 8: Zooming in on Future 1
Nuclear at $5100/kW does come in before 2030, but only 4GW
17.8GW by 2040
Over 20GW of CSP installed capacity in both scenarios

## Slide 9: Zooming in on Future 1

## Slide 10: Zooming in on Future 2
Delays: First unit in 2031
No new nuclear with flexible planning
CSP preferred at a cost of $7000/kW for nuclear
Imported hydro and shale gas

## Slide 11: Zooming in on Future 2
Sustained high electricity prices and crowding out of investment

Non-ferrous metals (-0.44% per annum)
Iron and steel (-0.21% per annum)
Metals (-0.17% per annum)
75 000 jobs at risk
Consumers are hit directly by electricity prices and by overall decreased growth

## Slide 12: Conclusions
Our results show that there is no economic case to be made for procuring the full 9.6GW of nuclear power by 2030.
High risk of electricity price increases with the commitment to nuclear power – 95th percentile.
As mentioned in the IRP Update and confirmed by our results, a flexible planning approach should be adopted.
The lock-in from a commitment a full fleet means that there is a trade off in investing in other least cost alternatives – putting pressure on the fiscus and South African tax payers.
The electricity build plan must reflect and balance the expected electricity demand, consider least-cost alternatives and ensure the provision of affordable electricity.
“Only procure nuclear at a scale and pace at which the country can afford.”

## Slide 13: Global nuclear power investment trends and why they matter for SA
Brenda Martin

## Slide 14: Nuclear power globally
Globally, nuclear accounts for about 10% of electricity production (down from a peak of 17% in the early 90s) (BP Statistical Review, 2015)
Nuclear’s contribution to global electricity production peaked in 2006 and has been slowly declining as fewer reactors are commissioned and older plants are retired
12% decline in energy produced since 2006 (peak predates the Fukushima accident)
The ‘nuclear renaissance’ is largely a myth
“world nuclear industry already faced daunting challenges long before Fukushima… starting with economics” (WNISR, 2014)
Notes: Also discuss WNISR – number of new reactors online, etc

## Slide 15: Cost trends
Latest nuclear plant in
UK (Hinkley Point) currently $8150/kW
Latest Russian reactor in Hungary currently $7031/kW

## Slide 16: Investment costs, LCOE and overruns
Investment costs and LCOE of nuclear currently higher than alternatives:
  Avg Gen III+ designs $7000/kW (WNISR, 2013)
  UK Hinkley Point £92.50/MWh (UK Gov Press Release)
  Turkey Akkuyu - built by the Russians: $123.5/MWh (NIW)
Imported hydro, coal, gas and renewables increasingly cheaper
  REIPPPP, round 4 wind bids dropped around 25%, solar PV around 29% (wind and solar averaged 60c/kWh (SAREC))
  Eskom wholesale average is about 80c/kWh
Notes: Explain LCOE – lcoe is a way of taking capital costs and operating costs and how many units the plant produces over its lifetime
To give you sense of how these numbers compare – under the REIPPPP, round 3 bids for wind averaged 66c/kWh, or 88c/kWh for PV. Current Eskom coal average is about half of that.
2008 tender figures at R1.50/kWh – signficantly hiher than the avg costs of electricity currently, even compared gainst solar PV and wind.
Overruns are the norm – over a third (23/66) reactors currently under construction have experienced construction delays.
But several reactors have been under construction for 10-20 years (or longer!)

## Slide 17: Investment costs, LCOE and overruns continued
Cost and time overruns on large capital-intensive projects like nuclear, coal
  Finland Olkiluoto 7 yrs behind schedule and 280% over budget (WNISR, 2014)
  France Flamanville 4 yrs late and cost has doubled (ibid)
  UAE Korean supplied reactors cost has doubled (NIW)
  Average construction time is 9.4 years (WNISR, 2014)
  Medupi and Kusile…
With nuclear, overruns are the norm – over a third (23/66) reactors currently under construction have experienced construction delays.
Of these, several reactors have been under construction for 10-20 years (or longer) (WNISR, 2014)
  Nuclear is not going to assist with SA’s current supply crisis

## Slide 18: Construction lead times for nuclear
Chart: 
| ANGRA-2 | DAYA BAY-1 | DAYA BAY-2 | FANGJIASHAN-1 | FUQING-1 | HONGYANHE-1 | HONGYANHE-2 | LING AO-1 | LING AO-2 | LING AO-3 | LING AO-4 | NINGDE-1 | NINGDE-2 | TIANWAN-1 | TIANWAN-2 | YANGJIANG-1 | TEMELIN-1 | TEMELIN-2 | CATTENOM-3 | CATTENOM-4 | CHOOZ B-1 | CHOOZ B-2 | CIVAUX-1 | CIVAUX-2 | GOLFECH-1 | GOLFECH-2 | PENLY-1 | PENLY-2 | KUDANKULAM-1 | TOMARI-3 | HANBIT-3 | HANBIT-4 | HANUL-3 | HANUL-4 | SHIN-KORI-1 | SHIN-KORI-2 | SHIN-WOLSONG-1 | BALAKOVO-4 | KALININ-3 | KALININ-4 | ROSTOV-1 | ROSTOV-2 | ROSTOV-3 | SIZEWELL B | KHMELNITSKI-2 | ROVNO-4 | COMANCHE PEAK-1 | COMANCHE PEAK-2 | SEABROOK-1 | WATTS BAR-1
Construction Years | 24.5151 | 6.0055 | 5.8411 | 5.9205 | 5.7507 | 5.5096 | 5.674 | 4.7589 | 4.8356 | 4.5836 | 4.9178 | 4.8356 | 5.1699 | 6.5863 | 6.6658 | 5.0027 | 13.8411 | 15.8411 | 8.0877 | 7.6685 | 12.5918 | 11.3397 | 9.1726 | 8.674 | 7.5863 | 8.6712 | 7.6685 | 7.5068 | 11.5945 | 4.3315 | 4.8356 | 5.1699 | 4.5068 | 5.0849 | 4.1699 | 4.589 | 4.1699 | 9.0055 | 19.1808 | 25.2685 | 19.5096 | 26.8521 | 5.2521 | 6.5918 | 19.5096 | 18.1808 | 15.3425 | 18.3452 | 13.8411 | 22.6027

## Slide 19: Nuclear power in South Africa
Koeberg: 2x900MW Framatome (Areva) units
Commissioned in ‘84 and ‘85
Supplies about 5% of South Africa’s electricity
Extensive safety upgrades after Fukushima accident
Planned: 9.6 GW new build, procurement pending

## Slide 20: IRP 2013 update on nuclear
“...demand may not reach the levels required which raises the risk of overbuilding generation capacity”
“…uncertainties suggest …a more flexible approach taking into account different outcomes based on changing…...scenarios and……in making key investment decisions”
“The nuclear decision can possibly be delayed…..and there are alternative options such as regional hydro…..before prematurely committing to a technology that may become redundant…..”
Notes: Historically (since the 1970s) , South Africa has overestimated demand growth. This has tended to result in the country overbuilding capacity – with significant impacts on the fiscus and consumers.

## Slide 21: Financing and risk
Financing
  Eskom balance sheet too weak to raise sufficient debt
  Fiscal and contingent liability constraints
  Current economic health: SA govt in no position to offer US or UK style loan guarantees or risk insurance
  Cost of capital generally higher than assumed discount rates (8%? 11%? Eskom bonds at 15%)
Risk allocation
  Unlike classic IPPs, nuclear vendors don’t take on primary cost risks: governments (consumers) do.
  When deals are structured so that vendors take the risk of cost overruns, the costs of actual bids have increased substantially
  High guaranteed tariffs are required, e.g. UK Hinkley Point
Notes: Discuss lack of private sector investment except with state subisidisation or guaranteed prices

## Slide 22: What do we propose?
Adopt dynamic, flexible, transparent electricity planning
Avoid locking-in with mega, capital-intensive power projects that come with risks of cost overruns and long and uncertain build timeframes
Invest in a diverse range of energy sources with shorter lead times that can be brought online incrementally to meet changing electricity demand
Practically, in South Africa, this means more investments in smaller coal, gas, renewable energy and energy efficiency
Notes: The IRP update ahs shown that when you use higher costs for nukes – costs that are in line with current global experience – the SA system should replace that capapcity with soalr, wind and gas (CCGT).
This is also supported by modelling done by the ERC – our New Power Plan estimates that nuclear power isnt reuired until 2029 at the earliest – and possibly not before 2040.

## Slide 23: Additional slides

## Slide 24: Finance models
Contracts for Differences:
  Still no deal at Hinkley. EDF has been saying for 6 years that it is close to making a FID, not in a position to do so.
Mankala model:
  Used in Finland and the Olkiluoto plant. Went horribly wrong in Finland – at least €6bn cost overrun.
  Non-profit model where the owners of the plant are large electricity users and who promise to buy the power at whatever cost.
The BOOT/BOO/BOT model:
  Never been used on a nuclear plant, the nearest is the deal between Russia and Turkey signed in 2010. Construction was expected to start then in 2011 but it has still to start and it is unsure if or when construction will start. Russia usually claims it can supply finance but it has spent all its money unsuccessfully defending the rouble.
China might be able to provide finance although the downturn there might make it more difficult. None of the other vendors can supply finance.
The ultimate guarantor will be the SA state and its credit rating is hovering on the junk status and signing up for 9600MW would almost certainly push it over the brink.

## Slide 25: Electricity demand
Chart: Annual Expected Electricity Consumption - upstream of transmission (TWh)
| 2015.0 | 2016.0 | 2017.0 | 2018.0 | 2019.0 | 2020.0 | 2021.0 | 2022.0 | 2023.0 | 2024.0 | 2025.0 | 2026.0 | 2027.0 | 2028.0 | 2029.0 | 2030.0 | 2031.0 | 2032.0 | 2033.0 | 2034.0 | 2035.0 | 2036.0 | 2037.0 | 2038.0 | 2039.0 | 2040.0
SO IRP moderate | 285.526 | 298.332 | 310.41 | 319.523 | 327.438 | 336.178 | 340.946 | 349.164 | 358.299 | 368.136 | 377.496 | 379.871 | 391 | 402.296 | 407.175 | 416.41 | 427.572 | 440.175 | 450.03 | 460.968 | 473.203 | 486.094 | 496.368 | 507.587 | 519.276 | 530.777
Best-Least.Cost | 269.1107 | #N/A | #N/A | #N/A | #N/A | 302.4928 | #N/A | #N/A | #N/A | #N/A | 341.3122 | #N/A | #N/A | #N/A | #N/A | 383.1398 | #N/A | #N/A | #N/A | #N/A | 444.3226 | #N/A | #N/A | #N/A | #N/A | 520.2344
Green Shoots | 271.424 | 279.384 | 287.479 | 296.379 | 305.418 | 314.79 | 324.303 | 333.929 | 343.561 | 353.651 | 364.056 | 366.034 | 376.611 | 387.506 | 398.408 | 409.14 | 418.001 | 425.856 | 433.743 | 440.862 | 447.926 | 454.617 | 461.389 | 468.272 | 473.96 | 479.589
SO IRP Low | 280.652 | 290.655 | 299.726 | 305.76 | 310.512 | 315.93 | 317.499 | 322.214 | 327.658 | 333.612 | 338.997 | 337.064 | 343.747 | 350.421 | 351.357 | 356.001 | 362.172 | 369.418 | 374.193 | 379.747 | 386.231 | 393.097 | 397.687 | 402.913 | 408.379 | 413.561
Worst-Least.Cost | 269.5436 | #N/A | #N/A | #N/A | #N/A | 297.3702 | #N/A | #N/A | #N/A | #N/A | 323.1436 | #N/A | #N/A | #N/A | #N/A | 341.3837 | #N/A | #N/A | #N/A | #N/A | 372.1124 | #N/A | #N/A | #N/A | #N/A | 404.4177
Weathering the Storm | 267.139 | 272.914 | 278.506 | 284.615 | 290.616 | 296.483 | 302.448 | 308.428 | 314.556 | 320.808 | 326.798 | 323.93 | 329.588 | 334.88 | 340.317 | 344.747 | 349.065 | 353.445 | 357.608 | 361.794 | 365.469 | 369.17 | 372.897 | 376.648 | 380.425 | 384.245

## Slide 26: Cost
Chart: Total Plant Cost in 2015 US$/kW
| IRP 2010 | EPRI IRP 2010 Low | EPRI IRP 2010 High | IEA2010 US High | EPRI 2008 | EIA 2008 | EIA 2009 | Lazard Low | Lazard High | MIT 2009 | IEA2010 Eur Low | IEA 2010 Eur High | EC2008 Low | EC2008 High | IEA2010 Asia Low | IES2010 Asia High | Finland Olkiluoto | France Flamanville | China Taishan | Hinkley Point | VVER-1200 lower | VVER-1200 upper
IRP Update | 5862.78 | 4234.23 | 4885.65 | 3691.38 | 4451.37 | 3691.38 | 5645.64 | 4125.66 | 5754.21 | 4451.37 | 4234.23 | 5862.78 | 2822.82 | 4885.65 | 1628.55 | 2497.11 | 6188.49 | 5862.78 | 2714.25 | 8685.6 | 0 | 0
Actual | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 7599.9 | 7599.9 | 0 | 0 | 0 | 0
Estimated | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2714.25 | 2931.39 | 0 | 0 | 5100.1843 | 7000.2136

## Slide 27: Lead Times
Chart: 
| ANGRA-2 | DAYA BAY-1 | DAYA BAY-2 | FANGJIASHAN-1 | FUQING-1 | HONGYANHE-1 | HONGYANHE-2 | LING AO-1 | LING AO-2 | LING AO-3 | LING AO-4 | NINGDE-1 | NINGDE-2 | TIANWAN-1 | TIANWAN-2 | YANGJIANG-1 | TEMELIN-1 | TEMELIN-2 | CATTENOM-3 | CATTENOM-4 | CHOOZ B-1 | CHOOZ B-2 | CIVAUX-1 | CIVAUX-2 | GOLFECH-1 | GOLFECH-2 | PENLY-1 | PENLY-2 | KUDANKULAM-1 | TOMARI-3 | HANBIT-3 | HANBIT-4 | HANUL-3 | HANUL-4 | SHIN-KORI-1 | SHIN-KORI-2 | SHIN-WOLSONG-1 | BALAKOVO-4 | KALININ-3 | KALININ-4 | ROSTOV-1 | ROSTOV-2 | ROSTOV-3 | SIZEWELL B | KHMELNITSKI-2 | ROVNO-4 | COMANCHE PEAK-1 | COMANCHE PEAK-2 | SEABROOK-1 | WATTS BAR-1
Construction Years | 24.5151 | 6.0055 | 5.8411 | 5.9205 | 5.7507 | 5.5096 | 5.674 | 4.7589 | 4.8356 | 4.5836 | 4.9178 | 4.8356 | 5.1699 | 6.5863 | 6.6658 | 5.0027 | 13.8411 | 15.8411 | 8.0877 | 7.6685 | 12.5918 | 11.3397 | 9.1726 | 8.674 | 7.5863 | 8.6712 | 7.6685 | 7.5068 | 11.5945 | 4.3315 | 4.8356 | 5.1699 | 4.5068 | 5.0849 | 4.1699 | 4.589 | 4.1699 | 9.0055 | 19.1808 | 25.2685 | 19.5096 | 26.8521 | 5.2521 | 6.5918 | 19.5096 | 18.1808 | 15.3425 | 18.3452 | 13.8411 | 22.6027
Notes: PRIS database

## Slide 28: Capacity schedule

## Slide 29: Availability
Chart: Availability (%)
| ANGRA-2 | DAYA BAY-1 | DAYA BAY-2 | FANGJIASHAN-1 | FUQING-1 | HONGYANHE-1 | HONGYANHE-2 | LING AO-1 | LING AO-2 | LING AO-3 | LING AO-4 | NINGDE-1 | NINGDE-2 | TIANWAN-1 | TIANWAN-2 | YANGJIANG-1 | TEMELIN-1 | TEMELIN-2 | CATTENOM-3 | CATTENOM-4 | CHOOZ B-1 | CHOOZ B-2 | CIVAUX-1 | CIVAUX-2 | GOLFECH-1 | GOLFECH-2 | PENLY-1 | PENLY-2 | KUDANKULAM-1 | TOMARI-3 | HANBIT-3 | HANBIT-4 | HANUL-3 | HANUL-4 | SHIN-KORI-1 | SHIN-KORI-2 | SHIN-WOLSONG-1 | BALAKOVO-4 | KALININ-3 | KALININ-4 | ROSTOV-1 | ROSTOV-2 | ROSTOV-3 | SIZEWELL B | KHMELNITSKI-2 | ROVNO-4 | COMANCHE PEAK-1 | COMANCHE PEAK-2 | SEABROOK-1 | WATTS BAR-1
2004 - 2014 | 86.1 | 85.1 | 84.2 | 79.6 | 81.1 | 88.5 | 89.6 | 83.9 | 87.7 | 75.3 | 83.8 | 86.3 | 72.5 | 77.8 | 79.2 | 82.1 | 79.7 | 80 | 76.5 | 80.5 | 82.5 | 83.6 | 81 | 82.3 | 43.4 | 87 | 89.1 | 87.5 | 80.1 | 75.3 | 73.7 | 72.9 | 78.5 | 83.3 | 81.5 | 87.2 | 90.5 | 83.9 | 77.1 | 73 | 89.7 | 91.8 | 87.6 | 90.2

## Slide 30: Centralised PV

## Slide 31: CSP

## Slide 32: Wind

## Slide 33: Nuclear Vendors

## Slide 34: Employment Assumptions